Buildroot image with Qt5 . OPEGN GLS 2.0 , mesa VC4 driver in 32 bit

Starting from the raspberry pi configuration for 32 bit:

make raspberrypi3_defconfig

nothing to be change in Target architecture

Change as usual the savedefconfig and download location

to the same place where all the builds you do. It could save time if downloaded package already there.

Before I will go over the QT5 VC4 settings, I will start with the compiler.
While adding QT5 in 32 bit I am getting compiler error when using external download compiler and external pre built

I tried to compile several times with external toolchain

But I got the following error when compiling with QT5 in the 32bit.
This is a problem of the compiler.

D_FILE_OFFSET_BITS=64 -Os --sysroot=/home/first/buildroot/blrpi3_32/buildroot-2017.05/output/host/usr/arm-buildroot-linux-gnueabihf/sysroot -O3 -O3 -std=c++1z -fvisibility=hidden -fvisibility-inlines-hidden -Wall -W -Wvla -Wdate-time -Wshift-overflow=2 -Wduplicated-cond -D_REENTRANT -fPIC -DQT_NO_USING_NAMESPACE -DQT_NO_FOREACH -DQT_USE_ICU -DQT_HAVE_POLL -DQT_HAVE_PPOLL -DQT_BUILD_CORE_LIB -DQT_BUILDING_QT -DQT_NO_CAST_TO_ASCII -DQT_ASCII_CAST_WARNINGS -DQT_MOC_COMPAT -DQT_USE_QSTRINGBUILDER -DQT_DEPRECATED_WARNINGS -DQT_DISABLE_DEPRECATED_BEFORE=0x050000 -D_LARGEFILE64_SOURCE -D_LARGEFILE_SOURCE -DQT_NO_DEBUG -I. -Iglobal -I../3rdparty/harfbuzz/src -I../3rdparty/md5 -I../3rdparty/md4 -I../3rdparty/sha3 -I../3rdparty/double-conversion/include -I../3rdparty/double-conversion/include/double-conversion -I../3rdparty/forkfd -I../../include -I../../include/QtCore -I../../include/QtCore/5.8.0 -I../../include/QtCore/5.8.0/QtCore -I.moc -I../../mkspecs/devices/linux-buildroot-g++ -o .obj/qhash.o tools/qhash.cpp
tools/qhash.cpp:148:54: error: attribute(target("+crc")) is unknown
 static uint crc32(const Char *ptr, size_t len, uint h)

to solve this I edit the qhash.cpp and add at the top
#undef __ARM_FEATURE_CRC32
This solve the compilation problem

The internal build root compiler , complains about other error that I don't konw why.
Never mind , I don't want the internal toolchain any case.

One thing left to check is external pre build compiler from cross tol ng for 32 bit
The armv8-rpi3-linux-gnueabihf

so I run cr-ng armv8-rpi3-linux-gnueabihf
and ct-ng build
to bulid that compiler.
Once does I will write about the success or not when compiling build root 32 bit + Qt5
with that compiler

Qt settings

VC4 is a DRM driver.

https://en.wikipedia.org/wiki/Direct_Rendering_Manager
From wikipedia

Enable mesa 3d in graphics libraries and applications

* from this list Gallium Etnaviv driver:

Enable the masa drivers
and the VC4 open gl driver by Broadcom.

The kernel Is configured as module = m

means , if the vc4 will find the Broadcom GPU it will be loaded.

QT5 configurations.
Enable qt quick

Loading overlays

If we dont load the vc4 overlay , the VC4 DRM driver will not be loaded.
And we will get from the raspberry pi 3 an error that DRM device was not loaded

in output/images/rpi-firmware/overlays

The VC4 driver needs is device tree blob
to load the device tree, open config.txt in output/images/rpi-firmware/config.txt

So in config.txt:

I will load two overlays
dtoverlay=pi3-miniuart-bt
dtoverlay=vc4-kms-v3d

There is a note:
# You should override this file using a post-build script.
I will deal with it later

output/images/rpi-firmware/cmdline.txt

I will add:
cma=128M
at the end

change:
gpu_mem_1024=256

When we use an overloay the VC4 DRI driver will load:

in buildroot mesa we need libinput

Running examples

Some examples does run but many don't for now

For example , the marron example in quick\demos
run on Ubuntu but not on my target raspberry pi 3.

update:

I have an SD card with raspbian jessie.
I enable using raspi-config the advanced settings for open gl
There we have two options:

We have the full KMS and fake KMS

like in the output/images/rpi-firmware/overlays
vc4-fkms-v3d.dtbo vc4-kms-v3d.dtbo

on the raspbian OS:
The full kms vc4-kms-v3d.dtbo does not work with neverball and also create lots of problem.
The fake KMS works but the mouse does not respond. ( the left click does not respond , while right click is ok )

So I changed in the buildroot to:
 dtoverlay=vc4-fkms-v3d

in config.txt

I justed capture with camera the back screen before it get completely white
and I saw that qtquickcontrol2/gallery complains about not having fonts in /usr/lib/fonts

The fonts will be installed to
/usr/share/fonts

>
> QFontDatabase: Cannot find font directory /usr/lib/fonts - is Qt
> installed correctly?
>
> Seems no fonts installed with Qt.
> Selected "liberation" package, but that installs the fonts to
> /usr/share/fonts
> Worked around by making a symlink from /usr/lib/fonts to there.
Fontconfig:
http://doc.qt.io/qt-5/qt-embedded-fonts.html

one option to solve the font problem is to create a link between /usr/share/fonts and /usr/lib/fonts

ln -s /usr/share/fonts /usr/lib/fonts
        source	link

maroon complains on png
so I added now all qt libraries

But remove qtengine because it did not compiled when I did make.
Could be that I can do make clean and make it will compile.
But seems that this library is not important.

http://doc.qt.io/archives/qt-5.5/enginio-index.html

qtwebkit also removed ( no support in the ARM)

Qt complains that it does not found libxbccommon
So I have added it now

Qt is complain that it cannod find the Physical with and height of the screen
After reading I found that the QT uses /dev/fb0 to determine the screen dimentions

So I have added:

Now I will test if those two errors will go away and I will have keyboard working..

Well , the keyboard and the resolution detection still not working

Adding Linux plug-in for QT

This solved the problem with the cannot detect the screen dimention

Adding

May be it will help Qt find the libxkbcommon to find the keyboard

Note: When in doubt, enable logging from both the graphics and input subsystems by setting the environment variable QT_LOGGING_RULES=qt.qpa.*=true before launching the application. This will help identifying the correct input device nodes and may uncover output configuration issues that can be difficult to debug otherwise.

QT_QPA_EGLFS_INTEGRATION=eglfs_brcm

QT_QPA_ENABLE_TERMINAL_KEYBOARD to 1
enable the control C

QT_QPA_EGLFS_PHYSICAL_WIDTH and QT_QPA_EGLFS_PHYSICAL_HEIGHT - Physical screen width and height in millimeters. On platforms where the value cannot be queried from the framebuffer device /dev/fb0 or via other means, a default DPI of 100 is used. This variable can be used to override any such defaults. Setting this is important because QWidget or Qt Quick Controls based applications rely on these values. Running with the hard-coded settings may result in user interface element sizes unsuitable for the display in use.

https://stackoverflow.com/questions/40490113/eglfs-on-raspberry2-failed-to-add-service-already-in-use

# What is the use of various Qt platform plugins?
https://stackoverflow.com/questions/21488072/what-is-the-use-of-various-qt-platform-plugins

export QML_IMPORT_TRACE=1

Font problem

When using buildroot , all fonts are installed in /usr/share/fonts

and QT is looking for them in /usr/lib/fonts

I tried to do a link from share/fonts to lib/fonts but it did not helped.

Only setting QT_QPA_FONTDIR to /usr/share/fonts/dejavu

https://forum.qt.io/topic/75145/cross-compile-qt-5-7-for-raspberry-pi-3-problem-font-text-words-in-application-not-showing-up-during-running/13

works!

Mouse keyboard problem

for now I dont have mouse and keyboard working in a simple quick gui

https://forum.qt.io/topic/47830/solved-no-input-on-linuxfb-and-eglfs/2

Mouse

In some examples, the mouse works but the mouse pointer is hidden.

Saving this configuration

make savedefconfig

will save to:

This I will upload to my github
https://github.com/EliArad/buildroot