Using raspberry pi 3 GPIO's

To the wifi image , I want to add GPIO support to togle some leds.

First , the pinout :

http://pi4j.com/pins/model-3b-rev1.html

There are resistors name r24 and capacitor c65 near the pin 1

mean while in build root we need to enable bcm2835

http://www.hobbytronics.co.uk/raspberry-pi-gpio-pinout
This is the correct for raspberry pi 3 model B

Wiring PI
http://wiringpi.com/

Great explanation here:

https://pinout.xyz/pinout/wiringpi

The wiring pi uses different pin numbering as describe in the link and can be use with python also

Enable wiring pi in buildroot

The GPIO utility
https://projects.drogon.net/raspberry-pi/wiringpi/the-gpio-utility/

maybe it is refereed to the one here in buildroot:

example code using several interfaces
http://elinux.org/RPi_GPIO_Code_Samples

Sysfs:

in make linux-menuconfig we can see that sysfs interface is already checked in

device drivers->gpio

The sysfs inteface shuold use the BCM numbering ( to check it)

using node js:

https://www.sitepoint.com/getting-started-with-the-raspberry-pi-gpio-pins-in-node-js/

Connecting Led

https://thepihut.com/blogs/raspberry-pi-tutorials/27968772-turning-on-an-led-with-your-raspberry-pis-gpio-pins

Must connect 330 Ohm to limit the current the the Led wants.

Raspberry pi 3 GPIO with Python.
http://makezine.com/projects/tutorial-raspberry-pi-gpio-pins-and-python/

Testing:

First with sys/class/gpio

I connected a led via a 400 Ohm resistor.
The ground to pin 49 and the positive of the led to pin 16.
pin 16 is gpio 23.

so:

echo 23 > /sys/class/gpio/export
echo out > /sys/class/gpio/gpio23/direction
echo 1 > /sys/class/gpio/gpio23/value

loop:

while true; do
echo 1 > /sys/class/gpio/gpio23/value
sleep 1
echo 0 > /sys/class/gpio/gpio23/value
sleep 1
done

And the led is toggling!!!!

With wiring pi:

using the gpio utility:

http://wiringpi.com/the-gpio-utility/

gpio -v
gpio version: 2.42
Copyright (c) 2012-2017 Gordon Henderson
This is free software with ABSOLUTELY NO WARRANTY.
For details type: gpio -warranty

Raspberry Pi Details:
  Type: Pi 3, Revision: 02, Memory: 1024MB, Maker: Embest
  * Device tree is enabled.
  *--> Raspberry Pi 3 Model B Rev 1.2
* This Raspberry Pi supports user-level GPIO access.

Wiring pi has different pin numbering for the same 40 pins header
for example

What I noticed is that the gpio command will not work if the sys/class/gpiox/export was not created!

So gpio is using the sys/class/ export and direction.

https://projects.drogon.net/raspberry-pi/wiringpi/the-gpio-utility/

Gpio 23 is wiring pi pin 4

so

gpio 23 is wiringip 4 . so we need to export gpio 23.
gpio is uing the /sys/class interface
gpio export 23 out
while true; do
gpio write 4 0
sleep 1
gpio write 4 1
sleep 1
done

will toggle the same led on gpio 23 ( wiring pi Pin 4) on and official

And yes, I can confirm that it is toggling.

Wiring pi in node js

First we need to set the date and time

also we need bash , node js and npm

date -s '2017-07-02 08:36:56'

https://github.com/Soarez/node-wiring-pi/blob/master/examples/pwm.js

trying to git clone:

git clone https://github.com/WiringPi/WiringPi-Node.git

Cloning into 'WiringPi-Node'...
fatal: Unable to find remote helper for 'https'

The easy place to see is in packages/git/git.mk
it is listed there one by one.