In order to try to use i2c in beaglebone , which is not working currently
I am trying to add the I2C2 device tree overlay

To use the overlay
1. We need to compile it
2. We can copy it from debain OS from /lib/firmware which it is compiled there (BB-I2C2-00A0.dtbo)

https://github.com/beagleboard/bb.org-overlays/blob/master/src/arm/BB-I2C2-00A0.dts

This is the overlays

/*
	* Copyright (C) 2013 CircuitCo
	*
	* Virtual cape for I2C2 on connector pins P9.19 P9.20
	*
	* This program is free software; you can redistribute it and/or modify
	* it under the terms of the GNU General Public License version 2 as
	* published by the Free Software Foundation.
	*/
	/dts-v1/;
	/plugin/;

	/ {
	compatible = "ti,beaglebone", "ti,beaglebone-black", "ti,beaglebone-green";

	/* identification */
	part-number = "BB-I2C2";
	version = "00A0";

	/* state the resources this cape uses */
	exclusive-use =
	/* the pin header uses */
	"P9.19", /* i2c2_sda */
	"P9.20", /* i2c2_scl */
	/* the hardware ip uses */
	"i2c2";

	fragment@0 {
	target = <&am33xx_pinmux>;
	__overlay__ {
	bb_i2c2_pins: pinmux_bb_i2c2_pins {
	pinctrl-single,pins = <
	0x178 0x73 /* i2c2_sda, SLEWCTRL_SLOW | INPUT_PULLUP | MODE3 */
	0x17c 0x73 /* i2c2_scl, SLEWCTRL_SLOW | INPUT_PULLUP | MODE3 */
	>;
	};
	};
	};

	fragment@1 {
	target = <&i2c2>;
	__overlay__ {
	status = "okay";
	pinctrl-names = "default";
	pinctrl-0 = <&bb_i2c2_pins>;

	/* this is the configuration part */
	clock-frequency = <100000>;

	#address-cells = <1>;
	#size-cells = <0>;

	/* add any i2c devices on the bus here */

	// commented out example of a touchscreen (taken from BB-BONE-LCD7-01-00A4) */
	// maxtouch@4a {
	// compatible = "mXT224";
	// reg = <0x4a>;
	// interrupt-parent = <&gpio4>;
	// interrupts = <19 0x0>;
	// atmel,irq-gpio = <&gpio4 19 0>;
	// };
	};
	};
	};

This is a cool site where we can create overlays dynamically
http://www.kilobaser.com/blog/2014-07-28-beaglebone-black-devicetreeoverlay-generator