Linux I2C Master with beaglebone black

The kw40z is now ready with software loaded and wired to be connected to my beaglebone black.

So in P9 connector with have SCL in pin 19 and
https://www.element14.com/community/thread/23991/l/bbb-i2c-notes?displayFullThread=true
I2C0: used for some on-board components (HDMI, EEPROM, power mgmt). Not brought out to any connector/header
I2C1: entirely free to use, but doesn't seem to be enabled
I2C2: entirely free to use, and works

I2C2 on Expansion header P9:
pin 19: SCL
pin 20: SDA
pin 1: 0V
pin 3: 3.3V