Raspberry pi 3 ultimate image

The image will contains:

wifii
bluetooth
qt5 open gl
git
node js
gpio
editors

Wi-Fi:
After adding the right components, I need to change the network/interfaces and wpa_supplicant.conf.

According to:
http://free-electrons.com/~thomas/buildroot/manual/html/ch04.html

board/raspberrypi/post-build.sh

Using that:
In the Buildroot configuration, you can specify the path to a post-build script, that gets called after Buildroot builds all the selected software, but before the rootfs packages are assembled. The destination root filesystem folder is given as the first argument to this script, and this script can then be used to copy programs, static data or any other needed file to your target filesystem.<br/>You should, however, use this feature with care. Whenever you find that a certain package generates wrong or unneeded files, you should fix that package rather than work around it with a post-build cleanup script.
I added:

cp interfaces ${TARGET_DIR}/etc/network

and the interfaces file is stored on the base_dir

# interface file auto-generated by buildroot

auto lo
iface lo inet loopback

auto eth0
iface eth0 inet dhcp
   pre-up /etc/network/nfs_check
   wait-delay 15

auto wlan0
iface wlan0 inet dhcp
        wireless-essid "Tenda_16A828"
        wireless-key "12345678"
        pre-up wpa_supplicant -i wlan0 -c /etc/wpa_supplicant.conf -B
        post-down killall -q wpa_supplicant

The same for wpa_supplicant.conf

I created a wpa_supplicate in the root directory:

ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=root
ctrl_interface_group=0
update_config=1

network={
        ssid="Tenda_16A828"
        psk="12345678"
        proto=WPA
        key_mgmt=WPA-PSK
        pairwise=CCMP
        auth_alg=OPEN
}
and add a line in post-build.sh

cp wpa_supplicant.conf ${TARGET_DIR}/etc/

Bluetooth:

In bluez5-utils the mk file should have:
BLUEZ5_UTILS_VERSION = 5.45
delete the hash file:
bluez5_utils.hash

make busybox-menuconfig
enable rfkill

Add in profile:

hciattach /dev/ttyAMA0 bcm43xx 115200 noflow -
hciattach /dev/ttyAMA0 bcm43xx 115200 noflow -

We should get Device setup complete and
rfkill list should show
hci0: bluetooth

hciconfig -a

For now I should call it twice. First time it failed ands second time completed success.

QT 5:

Qt5 required
dtoverlay=vc4-kms-v3d

For the mesa vc4 driver

I copied output/images/rpi-firmware/config.txt into root directory
and modified:

Change the config.txt to:

gpu_mem_1024=256
dtoverlay=vc4-kms-v3d

And add to post-build.sh

cp config.txt output/images/rpi-firmware/config.txt

For cmdline.txt

add
cma=128M

cmdline.txt will be also modified for blue tooth

we also need QT5 environment variables which we shell add to profile
copy profile to root and add:
export QT_QPA_FONTDIR=/usr/share/fonts/dejavu
export QT_QPA_ENABLE_TERMINAL_KEYBOARD=1
export QT_QPA_EGLFS_INTEGRATION=eglfs_kms
export QT_LOGGING_RULES=qt.qpa.*=true
export QT_QPA_PLATFORM=eglfs
export QT_QPA_EGLFS_PHYSICAL_WIDTH=100
export QT_QPA_EGLFS_PHYSICAL_HEIGHT=100

GPIO:

I created a script in /etc/ledblink

#!/bin/sh
gpio export 23 out
while true; do
gpio write 4 0
sleep 1
gpio write 4 1
sleep 1
done

this script will be copied to /etc/profile using the post-build.sh script

and add in profile :

chmod +x ./ledblink
./ledblink &

Testing the image

For WI-fi , if you set correctly your ssid and psk
Then you should see wlan0 and an valid IP on your network.

Type
ifconfig:

For Bluetooth:

type hciconfig -a

For QT-5

Run the maroon example.
It is one of the complicated examples

And also one of the qt control example.

For Git:

Just clone one.

For Gpio

The script should run after the login
root
eliarad
it will configure the gpio (23) ( wiring pi 4)
and start blinking.

We can also add it to inittab in many ways like:
::sysinit:/etc/ledblink &

For Node js:

you can clone:
https://github.com/EliArad/quicksite

npm install and bower install
and run node app.js

You can do it on your Ubuntu Linux and copy.
( npm on the target require clock setup correctly and some more configurations)

export GIT_SSL_NO_VERIFY=1

 After installing those packages , we should have the clock sync with ntp server

We also need more space for the application:
http://www.unitconversion.org/data-storage/gigabytes-to-blocks-conversion.html

So increase the number of blocks to what ever needs.

After cloning quicksite:
http://10.0.0.8:5000/#/

next step:

Add this package to buildroot.